## Slide 1: WSN@work Peter Van Aken / Alain Maes

## Slide 2: Topics
Building nodes (workshop 1.x)
  Exploring sensors/actuator
  Learning RF/electronics
  Writing firmware
Configuring controller (workshop 2.x)
Building gateway (workshop 3.x)
Use cases
  Demo
  Building

## Slide 3: Learning Arduino ?
USB book stick
Jeremy Blum : “arduino tutorial series” (https://www.youtube.com/watch?v=fCxzA9_kg6s)
Information source : https://www.arduino.cc/
Workshops 

## Slide 4
WSN@Work topology : workshops
Open SSID : WSNatWork
Wifi : auto channel
192.168.0.x
Controller
Gateway
(192.168.0.1)
LAN
Wireless Sensor Network
http(s)://192.168.0.107
1.x
2.x
3.x
Nodes

## Slide 5
WSN@Work to WSN@Home : roadmap
Open SSID : WSNatWork
Wifi : auto channel
192.168.0.x
(192.168.0.1)
LAN
http(s)://192.168.0.107
YOUR LED Node

## Slide 6
Open SSID : WSNatWork
Wifi : auto channel
192.168.0.x
YOUR Controller
Gateway
(192.168.0.1)
LAN
http(s)://192.168.0.107
YOUR LED Node

## Slide 7
Open SSID : WSNatWork
Wifi : auto channel
192.168.0.x
YOUR Controller
YOUR Gateway
(192.168.0.1)
LAN
http(s)://192.168.0.107
YOUR LED Node

## Slide 8: Platforms
Arduino (UNO, Nano, Pro mini)
Nordic NRF24L01+
1.x
Programming
Power
Programming
Power
5V / 16 MHz
3.3V / 8 MHZ (demo)

## Slide 9: Platform NRF24L01+ models
PA/LNA : ceramic / SMA antenna ; mini & DIL
  Open range : =< 1.1km
  Application : gateway, ptp long range, no battery operation
No PA/LNA : different antennas ; mini & DIL
  Open range : =< 100 m (in house : need meshing, don’t expect Wifi range !)
  Application : sensor nodes, with or without battery operation
1.x

## Slide 10: Platforms
Raspberry Pi v2.0 model B :
  SoC : BCM2836 (900MHz)
  1GB RAM
  100Mbps 802.3 / 4 x USB 2.0
  microSD
Accessories :
  PowerSupply : 5V+2A(!)
  microSD : >= 16GB Class 10 (!)
  Case (optional)
  HDMI cable / USB keyboard / mouse
UK product (Alie not recommanded for platform but accessories are OK)
2.x

## Slide 11: Platforms
Wired : Arduino Ethernet Shield W5100
Wifi : ESP8266 – NodeMCU ?
3.x

## Slide 12: Arduino Programming
In system programming (ISP)
Serial bootloader (Optiboot/…)
  Note : powered USB hub = extra protection
  On board USB
  FDTI (http://nl.aliexpress.com/item/Free-Shipping-1PCS-FT232RL-FT232-USB-TO-TTL-5V-3-3V-Download-Cable-To-Serial-Adapter/32340783857.html?ws_ab_test=searchweb201556_6_79_78_77_82_80_62,searchweb201644_0,searchweb201560_5)
OTA bootloader
  MysBootloader
  DualOptiboot

## Slide 13: ISP programming & fuse bits
USBtinyisp (with Arduino 1.6.5)
  Burn bootloader
AVRisp mkII (AVR studio 4)
  http://www.engbedded.com/fusecalc/
  Fuse bits
Avr Dragon (AVR studio 4)
  Debugging

## Slide 14: LED node : code walk
Initialisation :
Presentation :
Sending/Receiving data :

## Slide 15: Node addressing (RF)
Nordic Enhanced ShockBurst format
Address = WSN base@ (4bytes) || NodeId (1byte) (0/255 reserved)
  WSNbase
  2^32 WSNs with (254 nodes / freq) ; behind 1IP@
Distance vector based routing (EEPROM) : node2node distance = 1

## Slide 16: e2e WSNatWork stack
wired
RF

## Slide 17: Packet Walk : node debug
  MyConfig.h (SERIAL DEBUG)
    Disable = 6% extra flash !
  MYScontroller (demo) !! gateway interaction !!
    http://www.mysensors.org/controller/myscontroller
  NRF24 sniffer (demo : see next slide)
    http://forum.mysensors.org/topic/242/wireless-nrf24l01-sniffer-for-mysensors

## Slide 18: LED node : wireshark air capture