## Slide 1: WSN@work Peter Van Aken

## Slide 2: Topics
Building nodes
  Exploring sensors/actuator
  Learning RF/electronics
  Writing firmware
Configuring controller
Building gateway
Use cases
  Demo
  Building

## Slide 3: Platforms
Arduino (UNO, Nano, Pro mini, Mega…)
ESP8266 (ESP-3/12/…)
Raspberry Pi, BeagleBone black
…

## Slide 4
WSN@Work topology
Open SSID : WSNatWork
Wifi : auto channel
192.168.0.x
Controller
(192.168.0.107)
MQTT client Gateway
(192.168.0.225)
(192.168.0.1)
LAN
Wireless Sensor Network
ISM (Industrial Scientific Medical) license-free band
Channel 76
(2.476Ghz)
Sensor / Actuator node
Repeater node
selfhealing
meshing
w/battery powered
http(s)://192.168.0.107
(wsn / 1234)

## Slide 5: Learning Arduino ?
USB book stick
Jeremy Blum : “arduino tutorial series” (https://www.youtube.com/watch?v=fCxzA9_kg6s)
Information source : https://www.arduino.cc/
Workshops 

## Slide 6: ATMEL Atmega328p versus Arduino UNO
Wh at is an “Arduino UNO” :
  Cheap open source fast prototyping platform
  Based on Atmega328p + USB/serial + power
  Arduino IDE
Arduino variants :
  Mega, Micro PRO, Nano, … (see boards : Arduino IDE)

## Slide 7: Arduino IDE
Installation :
  Windows : https://www.arduino.cc/en/Guide/Windows
  MaxOS : https://www.arduino.cc/en/Guide/MacOSX
  Linux : http://playground.arduino.cc/Learning/Linux
Examples : “blinking Led”
Connect your LED to pin 2 & change code
2

## Slide 8: Arduino IDE alternative
AVR studio

## Slide 9: ATMEL Atmega328p
Datasheet : http://www.atmel.com/images/atmel-8271-8-bit-avr-microcontroller-atmega48a-48pa-88a-88pa-168a-168pa-328-328p_datasheet_complete.pdf
Memory map : 32KB flash 2KB RAM 1KB EEprom

## Slide 10: Arduino Programming
In system programming (ISP)
Serial bootloader (Optiboot/…)
  Note : powered USB hub = extra protection
OTA bootloader
  MysBootloader
  DualOptiboot

## Slide 11: Arduino UNO reference https://arduino-info.wikispaces.com/QuickRef

## Slide 12: “The Radio” : Nordic NRF24L01+
Datasheet : http://www.nordicsemi.com/eng/Products/2.4GHz-RF/nRF24L01P
Highlights :
  2.4Ghz – 2.525Ghz : stay out Wifi band !
  250 kbps (only+!), 1Mbps, 2Mbps
  Low power : 1.9 – 3.6v, I/Os 5V tolerant
    Breakout/adaptor : 3.3v - 12V
    Vcc filter capacitor

## Slide 13: Wiring (SPI interface)

## Slide 14: Node firmware : MySensors
http://www.mysensors.org/
Download :
  Mysensors v1.5 : http://www.mysensors.org/download/
  “node test”
    MyConfig.h
    Code walk
    Change NodeId & go