## Slide 1: WSN@work Gateway prototyping Peter Van Aken/Alain Maes

## Slide 2: Wemos & protoshield

## Slide 3: Wemos & protoshield
Pro :
  LDO can power for NRF with PA
  Integrated serial-(micro)USB
  Easy access to GPIO
  Arduino (proto)shield compatible
  SOIC footprint for ATSHA204
Con :
  A bit of soldering when using shield
  No run/flash switch (stability test)

## Slide 4: Wemos & protoshield
Alie:
  Wemos :
    http://nl.aliexpress.com/item/WeMos-D1-WiFi-uno-based-ESP8266-for-arduino-Compatible/32458787267.html
  Shield : “arduino proto shield”
Ebay:
  Wemos : http://www.benl.ebay.be/itm/221949739425?clk_rvr_id=977251000263&rmvSB=true
  Shield :
  http://www.benl.ebay.be/itm/381382884053?clk_rvr_id=977239437874&rmvSB=true

## Slide 5: ESP8266 test board with IO leads

## Slide 6: ESP8266 test board with IO leads
Pro :
  Easy powering via battery / mobile
  Run/Flash switch
  LDR/RGB led (learn ESP, not GW specific)
  No soldering
Con :
  No standard shield form factor
  NRF with PA not possible (LDO limited power)
  External USB-serial required
  SOIC breakout for ATSHA204

## Slide 7: ESP8266 test board with IO leads
Alie :
  Board: http://nl.aliexpress.com/item/ESP8266-ESP-12E-serial-WIFI-Industrial-stable-version-A-full-test-board-Full-IO-leads/32370570377.html
  USB-serial :

## Slide 8: NodeMCU

## Slide 9: NodeMCU
Pro :
  Easy to connect to GPIOs via breadboard. No soldering.
  USB-serial integrated
Con :
  No Run/Flash switch
  Powering NodeMCU with NRF PA attached gave problems for me (*)
  SOIC breakout for ATSHA204

## Slide 10: NodeMCU
Alie :
  http://nl.aliexpress.com/item/V2-4M-4FLASH-NodeMcu-Lua-WIFI-Networking-development-board-Based-ESP8266/32448662166.html

## Slide 11: Full breadboard

## Slide 12: Full breadboard
Pro :
  Easy to connect to GPIOs via breadboard, very flexible.
  “unlimited” power from supply
  Run/Flash switch
Con :
  Limited soldering
  SOIC breakout for ATSHA204
  External USB-serial

## Slide 13: Full breadboard
Alie:
  ESP12:
  Breakout:
  USB-serial:
  Power supply:
  RTC
  OLED
  ATSHA204

## Slide 14: Arduino UNO / Ethernet shield

## Slide 15: Arduino UNO / Ethernet shield
Pro :
  Easy to connect (see also Wemos protoshield)
  Plug & play
Con :
  Ethernet connection required
  Limited configuration & extention options
    Hardcoded settings
    Memory footprint > 90 % (on nano 96% !!)
  Power consumption ethernet shield

## Slide 16: Arduino UNO / Ethernet shield
Alie:
  Ethernet : http://nl.aliexpress.com/item/W5100-Ethernet-Shield-for-Arduino-Main-Board-UNO-R3-ATMega-328-1280-MEGA2560-1Pc/32417441214.html?spm=2114.010208.3.28.npM0nn&ws_ab_test=searchweb201556_9,searchweb201644_4_505_506_503_504_301_502_10014_10001_10002_10016_10017_10010_10005_10011_10006_10003_10004_401_10009_10008,searchweb201560_3,searchweb1451318400_-1,searchweb1451318411_6448&btsid=c4c77b18-21f4-426b-aefa-c9472589e6d0
Remark : Ethernet shield 2. (wiznet W5500)