## Slide 1: WSN@work LED-node 2.0 Jo Simons

## Slide 2: What’s the target
Build a LED node which
  supports multiple commands to a LED
  sends feedback with actual LED status
  sends periodic updated counter
Configure OpenHab with
  command buttons iso an on/off switch
  live LED status based on node feedback
Provide cross-platform MQTT client for testing
Based on wireless MySensorsGateway

## Slide 3: End-2-end view

## Slide 4: LED node 2.0
This node accepts following commands:
  value 2: turn LED on
  value 3: turn LED off
  value 6: toggle LED
  value 9: start LED blinking
This node will send:
  new counter value every second
  current LED state when this is changed (0=off,1=on)

## Slide 5: Arduino code 1/5
Variables and defines
  #include <DigitalIO.h>
  #include <DigitalPin.h>
  #include <MySensor.h>
  #include <SPI.h>
  #define CNT_ID 0 // counter sensor id
  #define LED_ID 1 // LED sensor id
  #define LED_PIN 2 // LED pin
  #define LED_OFF 0 // LED off state
  #define LED_ON 1 // LED on state
  #define LED_BLINK 2 // LED blinking indicator, ored with state
  #define NODE_ID 31 // CHANGE TO YOUR NODE-ID !!!
  MySensor gw;
  MyMessage eventMsg(CNT_ID, V_VOLUME);
  MyMessage statusMsg(LED_ID, V_LIGHT);
  unsigned long lastUpdate = 0;
  int cntValue = 0;
  int ledState = LED_OFF;

## Slide 6: Arduino code 2/5
Initialise the node
  void setup() {
  Serial.begin(115200);
  Serial.println("start serial");
  // startup and initialize MySensors library.
  gw.begin(handleIncMsg, NODE_ID, false);
  gw.sendSketchInfo("ledNode", "2.0");
  gw.present(CNT_ID, S_WATER); // -> V_VOLUME
  gw.present(LED_ID, S_LIGHT); // <> V_LIGHT
  // initialize the LED with reloaded state from EEPROM
  pinMode(LED_PIN, OUTPUT);
  setLED(ledState = gw.loadState(LED_ID));
  Serial.println("init done");
  gw.process();
  } // setup

## Slide 7: Arduino code 3/5
Set LED and send feedback
  void setLED(int nState) {
  // write to output
  digitalWrite(LED_PIN, nState & LED_ON);
  // send on/off feedback to gateway
  gw.send(statusMsg.setSensor(LED_ID).set(nState & LED_ON));
  // save full state to EEPROM and report
  gw.saveState(LED_ID, nState);
  Serial.print("LED state=");
  Serial.println(nState);
  } // setLED

## Slide 8: Arduino code 4/5
Periodical processing
  void loop(){
  unsigned long now = millis();
  if ((now - lastUpdate) > 1000) {
  // update counter every second
  gw.send(eventMsg.setSensor(CNT_ID).set(++cntValue));
  Serial.println(cntValue);
  lastUpdate = now;
  // handle blinking LED
  if (ledState & LED_BLINK)
  setLED(ledState = ((ledState & LED_ON) ? LED_OFF : LED_ON) | LED_BLINK);
  }
  // Alway process messages whenever possible
  gw.process();
  } // loop

## Slide 9: Arduino code 5/5
Handling command from controller
  void handleIncMsg(const MyMessage &incMsg) {
  if ((incMsg.type == V_LIGHT) && (incMsg.sensor == LED_ID)) {
  Serial.print("LED command=");
  Serial.print(incMsg.getInt());
  switch (incMsg.getInt()) {
  case 2: ledState = LED_ON;
  break;
  case 3: ledState = LED_OFF;
  break;
  case 6: ledState = (ledState & LED_ON) ? LED_OFF : LED_ON;
  break;
  case 9: ledState = ((ledState & LED_ON) ? LED_OFF : LED_ON) | LED_BLINK;
  break;
  default: Serial.print("... unknown command");
  break;
  } // switch
  Serial.println("");
  setLED(ledState);
  }
  } // handleIncMsg

## Slide 10: Wireless GW MQTT Settings
Goto http://<ip-address-of-gateway>/mqttconfig
From sensor prefix: evtMQTT
  messages coming from the LED node will be published as:
    evtMQTT/<node>/<sensor>/<type>=<val>
  samples:
    evtMQTT/31/0/V_VOLUME=1234
    evtMQTT/31/1/V_LIGHT=0
From controller prefix: cmdMQTT
  the GW will subscribe to cmdMQTT/* topics
  published messages are passed through to the LED node:
    cmdMQTT/31/1/V_LIGHT=2 turns LED on
    cmdMQTT/31/1/V_LIGHT=3 turns LED off
    cmdMQTT/31/1/V_LIGHT=6 toggles LED
    cmdMQTT/31/1/V_LIGHT=9 starts LED blinking

## Slide 11: OpenHab Configuration 1/3
Items
  defined in: configurations/items/test.items
  structured naming: node<node-id>_<sensor-type><sensor-id>
    i.e. node31_cnt0, node31_led1, node31_fb1
  we define 3 items
    node31_cnt0 for the counter that is updated every second
    node31_fb1 for receiving the feedback of actual LED state
    node31_out1 for controlling the LED, describing all supported commands
  Number node31_cnt0 " [%d]" { mqtt="<[mysensor:evtMQTT/31/0/V_VOLUME:state:default]" }
  Number node31_fb1 " [%d]" { mqtt="<[mysensor:evtMQTT/31/1/V_LIGHT:state:default]" }
  Switch node31_out1 "" { autoupdate="false“, mqtt=">[mysensor:cmdMQTT/31/1/V_LIGHT:command:ON:2],>[mysensor:cmdMQTT/31/1/V_LIGHT:command:OFF:3],>[mysensor:cmdMQTT/31/1/V_LIGHT:command:TOGGLE:6] ,>[mysensor:cmdMQTT/31/1/V_LIGHT:command:BLINK:9]" }

## Slide 12: OpenHab Configuration 2/3
Sitemap
  defined in: configurations/sitemaps/default.sitemap
  describes the layout of the UI
  uses a Text field to display the periodic timer update
  uses a Switch field with mappings to display the 3 command buttons
  OpenHab implied behaviour of Toggle !!!
  Text label="Simonjo" icon="boy0" {
  Frame {
  Text item=node31_cnt0 label="cnt0 [%d]" icon="calendar"
  Switch item=node31_out1 label="out1" icon="light" mappings=[ON="On", OFF="Off", TOGGLE="Toggle"]
  }
  }

## Slide 13: OpenHab Configuration 3/3
Rule
  defined in: configurations/rules/test.rules
  converts the update received for item ‘node31_fb1’ into an update for the icon of item ‘node31_out1’
  // map LED node feedback onto icon
  rule "node31_fb1"
  when
  Item node31_fb1 received update
  then
  node31_out1.postUpdate(if(node31_fb1.state.toString == "1") ON else OFF)
  end

## Slide 14: OpenHab GUI
Previous configuration will result in this GUI

## Slide 15: MQTT client for testing
Cross platform
  Windows xmqttc.exe
  Linux on x86 xmqttc.x86
  RaspberryPi (ARM) xmqttc.raspi
  Onion Omega (MIPS) xmqttc.onion
Get help: ./xmqtt.raspi -?
  Important to specify unique --clientid <clientid>
  And to specify target MQTT broker with --remaddr <ip-addr>
Sample usage:
  ./xmqttc.raspi --clientid simonjo --remaddr <ip-addr-broker> cmdMQTT/31/1/V_LIGHT=6