## Slide 1: WSN@work the controller Peter Van Aken

## Slide 2
Sensor / Actuator node
Repeater node
WSN@Work topology
Open SSID : WSNatWork
192.168.0.x
Controller
(192.168.0.107)
MQTT client Gateway
(192.168.0.225)
(192.168.0.1)
LAN
Wireless Sensor Network
ISM (Industrial Scientific Medical) license-free band
Channel 76
(2.476Ghz)
selfhealing
meshing
w/battery powered
http(s)://192.168.0.107
Wifi : auto channel
LED-nodes

## Slide 3: Topics
Getting your Raspberry Pi 2 ready
Installing OpenHab
MQTT as bridge

## Slide 4: Getting your RPiV2 ready
Info source : https://www.raspberrypi.org
Install methods :
  NOOBS : OR
    https://www.raspberrypi.org/help/noobs-setup/
    Select your OS during PI startup
  Native (Raspian) (my preference)
Workflow for both methods is the same :
  Install an SD write on your OS (Linux/Mac/Windows)
  Burn .img to SD
  Boot Rpi with SD and configure
BACKUP : done with the same SD writer !! (keep a base image)

## Slide 5: Getting your RPiV2 ready
“sudo raspi-config” is your best friend
  1 : expand filesystem
  5 : internationalisation options
    I1 : nl_BE@euro ISO_8859_15
    I2 : Europe/Brussel
    I3 : keyboard (!! Default is QWERTY)
reboot
  6 : enable camera (if available)
  9 : advanced options
    A4 : enable SSH
  2 : change user passwd
reboot

## Slide 6: Getting your RPiV2 ready
Network access :
  Wired : woks out-of-the box
  Wireless : https://www.raspberrypi.org/documentation/configuration/wireless/wireless-cli.md
SSH with root :
  Set passwd : sudo passwd root
  In /etc/ssh/sshd_config : search for “PermitRootLogin” and change this to “yes”
Now SSH access is working for both users
sudo apt-get update
sudo apt-get upgrade
READY to run headless : backup base image

## Slide 7: Getting your RPiV2 ready
SSH / file transfer tools :
  FileZilla, Putty, BitVise (https://www.bitvise.com/download-area), ....

## Slide 8: Getting your RPiV2 ready : optional
VNC
  sudo apt-get install tightvncserver
  start once to set passwd
    vncserver :1 –geometry 1920x1080 –depth 24
  Automatic start during boot :
    copy “vncstart” to /etc/init.d in your PI
    sudo chmod +x /etc/init.d/vncstart
    sudo update-rc.d vncstart defaults
OR : https://www.raspberrypi.org/documentation/remote-access/vnc/
This is my base image backup

## Slide 9: Getting your RPiV2 ready : optional
Windows SD image backup tool : https://www.google.be/?gws_rd=ssl#q=win32diskimager
Linux : google & add
MacOS : google & add

## Slide 10: Getting your RPiV2 ready : optional
Samba : http://raspberrywebserver.com/serveradmin/share-your-raspberry-pis-files-and-folders-across-a-network.html
Change hostname : http://raspberrywebserver.com/serveradmin/change-your-pis-host-name.html
Backup data to “the Cloud” : http://raspberrywebserver.com/serveradmin/back-up-your-pi-to-your-google-drive.html
Touchscreen keyboard :
  sudo apt-get install matchbox
GVIM :
  sudo apt-get install vim-gui-common

## Slide 11: Getting your RPiV2 ready : optional
Extend SD card lifetime : http://www.zdnet.com/article/raspberry-pi-extending-the-life-of-the-sd-card/

## Slide 12: Static IP@ for the workshop
(100 + YOUR NodeID)
Add
(see NodeIdAllocation.txt)

## Slide 13: Installing Openhab
Info source : http://www.openhab.org/

## Slide 14: Installing Openhab
Copy “Openhab 1.8.0” folder under /home/pi (ssh/...)
This folder includes :
  demo
  addons used in WSN. Add from “Openhab 1.8.0 Addons” depending upon your need. Startup-time !
In /home/pi/Openhab 1.8.0 : chmod 755 *.sh

## Slide 15: Configuring Openhab : security
/home/pi/Openhab 1.8.0/configuration/openhab.cfg
/home/pi/Openhab 1.8.0/configuration/users.cfg

## Slide 16: Configuring Openhab : SMTP
/home/pi/Openhab 1.8.0/configuration/openhab.cfg
...this will allow Openhab to send you emails based on rules...

## Slide 17: Configuring Openhab : SMTP
Example rule : no need to add for workshop

## Slide 18: Configuring Openhab : MySQL
/home/pi/Openhab 1.8.0/configuration/openhab.cfg
this will allow Openhab to store sensor data
MySQL can be running remotely or on NAS device. In this example it’s local in Rpi
See optional section for MySQL installation

## Slide 19: Configuring Openhab : MQTT
/home/pi/Openhab 1.8.0/configuration/openhab.cfg
Point to the location were your MQTT broker (e.g. Mosquitto) is running. This must be synced with the gateway.
For WSNatWork workshop : stick to this IP@
...these are the basic to get WSNatWork up and running but there is much, much more inside...
ClientId must
be UNIQUE
In network

## Slide 20: Configuring Openhab : port
/home/pi/Openhab 1.8.0/start.sh
  sudo vi start.sh (same for start_debug.sh)

## Slide 21: Start Openhab
In /home/pi/Openhab 1.8.0/configuration/
  Without debug : sudo ./start.sh
  With debug : sudo ./start_debug.sh

## Slide 22: Connect to Openhab

## Slide 23: Moving your LED-node into Openhab

## Slide 24: Internals : e2e WSNatWork stack
Wired/ Wireless
RF

## Slide 25: Internals : MQTT broker
WSNatWork is using Mosquitto 3.1.1. (free open source SW)
About MQTT :

## Slide 26: Internals : MQTT broker
Basic concept in a nutshell :
  works with topics (MyMQTT/22/1/V_VOLUME...)
  MQTT clients subscribe to interesed topics in MQTT broker
  MQTT clients publish topics to MQTT broker
  MQTT broker publishes topics to subscribed MQTT clients (kind of multicast)
Very good explanation : http://www.hivemq.com/blog/mqtt-essentials/ (part 1 – 11)
MQTT Client
MQTT Client
MQTT Broker

## Slide 27: Openhab and persistency
Not restricted to single data storage : MySQL, cloud, ... (see https://github.com/openhab/openhab/wiki/Persistence)
In WSN-at-Work :
  RR4DJ : is a high performance data logging and graphing system for time series data. Ideal to get trend on low BW devices (eg smartphone in radio network)
  MySQL : accurate logging
Configuration :

## Slide 28: Openhab and persistency

## Slide 29: Openhab and persistency
Demo using HABMIN to query persistent data
From internet explorer using MySQL: (apache2 has to be running !!)

## Slide 30: Openhab and persistency
From Smartphone using RR4DJ :

## Slide 31: Openhab and persistency
Exercise : make your LED-node counter persistent

## Slide 32: Openhab and rules
”Rules” are used for automating processes (see : https://github.com/openhab/openhab/wiki/Rules#introduction)
Location :
Different ways to trigger : item, time, system event, ...

## Slide 33: Openhab and rules
Samples :

## Slide 34: Openhab and rules
Exercises :
  Automate your LED on your LED-node to turn on/off every minute.
  Send yourself an email if the node is turned on.

## Slide 35: Optional

## Slide 36: Openhab @ startup

## Slide 37: Habmin
Already included :
  http:<your Openhab ip>/habmin
Alternative :

## Slide 38: MySQL
- install : sudo apt-get install mysql-server
add openhab user: mysql –u root –p
  create database openhab;
  CREATE USER 'openhab'@'localhost' IDENTIFIED BY 'openhab';
  GRANT ALL PRIVILEGES ON openhab.* TO 'openhab'@'localhost';
tips :
- Drop database : drop database if exists openhab;
- Select database : use openhab;
- Show tables : show tables;
- Create database : create database openhab;

## Slide 39: Wireshark & MQTT
see :
  https://github.com/menudoproblema/Wireshark-MQTT
start :
wireshark -X lua_script:mqtt.lua
capture :
mqtt.publish.topic matches "MyMQTT/69/6"
prefix
nodeId
sensor

## Slide 40: MQTT broker : Mosquitto
sudo apt-get install mosquitto mosquitto-clients python-mosquitto
sudo /etc/init.d/mosquitto stop
start :

## Slide 41: MQTT broker : Mosquitto on Synology NAS

## Slide 42: MQTT broker / live capture using wireshark
(LED) node
Gateway
MQTT broker
(192.168.0.107)
Openhab (see your IP@)
see air capture workshop 1.1
connect
publish
publish
publish